## Slide 1: Computer Organization & Assembly Language - EE2003

## Slide 2: Lecture 16
Week 10

## Slide 3: Chapter Overview
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and Unpacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 4: Shift and Rotate Instructions
Logical vs Arithmetic Shifts
SHL Instruction
SHR Instruction
SAL and SAR Instructions
ROL Instruction
ROR Instruction
RCL and RCR Instructions
SHLD/SHRD Instructions

## Slide 5: Logical Shift
A logical shift fills the newly created bit position with zero:

## Slide 6: Arithmetic Shift
An arithmetic shift fills the newly created bit position with a copy of the number’s sign bit:

## Slide 7: SHL Instruction
The SHL (shift left) instruction performs a logical left shift on the destination operand, filling the lowest bit with 0.
Operand types for SHL:
SHL reg,imm8
SHL mem,imm8
SHL reg,CL
SHL mem,CL
(Same for all shift and rotate instructions)

## Slide 8: Fast Multiplication
mov dl,5
shl dl,1
Shifting left 1 bit multiplies a number by 2
mov dl,5
shl dl,2 ; DL = 20
Shifting left n bits multiplies the operand by 2n
For example, 5 * 22 = 20

## Slide 9: SHR Instruction
The SHR (shift right) instruction performs a logical right shift on the destination operand. The highest bit position is filled with a zero.
mov dl,80
shr dl,1 ; DL = 40
shr dl,2 ; DL = 10
Shifting right n bits divides the operand by 2n

## Slide 10: SAL and SAR Instructions
SAL (shift arithmetic left) is identical to SHL.
SAR (shift arithmetic right) performs a right arithmetic shift on the destination operand.
An arithmetic shift preserves the number's sign.
mov dl,-80
sar dl,1 ; DL = -40
sar dl,2 ; DL = -10

## Slide 11: Your turn . . .
mov al,6Bh
shr al,1 a.
shl al,3 b.
mov al,8Ch
sar al,1 c.
sar al,3 d.
Indicate the hexadecimal value of AL after each shift:
35h
A8h
C6h
F8h

## Slide 12: ROL Instruction
ROL (rotate) shifts each bit to the left
The highest bit is copied into both the Carry flag and into the lowest bit
No bits are lost
mov al,11110000b
rol al,1 ; AL = 11100001b
mov dl,3Fh
rol dl,4 ; DL = F3h

## Slide 13: ROR Instruction
ROR (rotate right) shifts each bit to the right
The lowest bit is copied into both the Carry flag and into the highest bit
No bits are lost
mov al,11110000b
ror al,1 ; AL = 01111000b
mov dl,3Fh
ror dl,4 ; DL = F3h

## Slide 14: Your turn . . .
mov al,6Bh
ror al,1 a.
rol al,3 b.
Indicate the hexadecimal value of AL after each rotation:
B5h
ADh

## Slide 15: RCL Instruction
RCL (rotate carry left) shifts each bit to the left
Copies the Carry flag to the least significant bit
Copies the most significant bit to the Carry flag
clc ; CF = 0
mov bl,88h ; CF,BL = 0 10001000b
rcl bl,1 ; CF,BL = 1 00010000b
rcl bl,1 ; CF,BL = 0 00100001b

## Slide 16: RCR Instruction
RCR (rotate carry right) shifts each bit to the right
Copies the Carry flag to the most significant bit
Copies the least significant bit to the Carry flag
stc ; CF = 1
mov ah,10h ; CF,AH = 1 00010000b
rcr ah,1 ; CF,AH = 0 10001000b

## Slide 17: Your turn . . .
stc
mov al,6Bh
rcr al,1 a.
rcl al,3 b.
Indicate the hexadecimal value of AL after each rotation:
B5h
AEh

## Slide 18: SHLD Instruction
Shifts a destination operand a given number of bits to the left
The bit positions opened up by the shift are filled by the most significant bits of the source operand
The source operand is not affected
Syntax:
  SHLD destination, source, count
Operand types:
SHLD reg16/32, reg16/32, imm8/CL
SHLD mem16/32, reg16/32, imm8/CL

## Slide 19: SHLD Example
Shift count of 1:
mov al,11100000b
mov bl,10011101b
shld al,bl,1

## Slide 20: Another SHLD Example
.data
wval WORD 9BA6h
.code
mov ax,0AC36h
shld wval,ax,4
Shift wval 4 bits to the left and replace its lowest 4 bits with the high 4 bits of AX:
Before:
After:

## Slide 21: SHRD Instruction
Shifts a destination operand a given number of bits to the right
The bit positions opened up by the shift are filled by the least significant bits of the source operand
The source operand is not affected
Syntax:
  SHRD destination, source, count
Operand types:
SHRD reg16/32, reg16/32, imm8/CL
SHRD mem16/32, reg16/32, imm8/CL

## Slide 22: SHRD Example
Shift count of 1:
mov al,11000001b
mov bl,00011101b
shrd al,bl,1

## Slide 23: Another SHRD Example
mov ax,234Bh
mov dx,7654h
shrd ax,dx,4
Shift AX 4 bits to the right and replace its highest 4 bits with the low 4 bits of DX:
Before:
After:

## Slide 24: Your turn . . .
mov ax,7C36h
mov dx,9FA6h
shld dx,ax,4 ; DX =
shrd dx,ax,8 ; DX =
Indicate the hexadecimal values of each destination operand:
FA67h
36FAh

## Slide 25: What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and Unpacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 26: Shift and Rotate Applications
Shifting Multiple Doublewords
Binary Multiplication
Displaying Binary Bits
Isolating a Bit String

## Slide 27: Shifting Multiple Doublewords
Programs sometimes need to shift all bits within an array, as one might when moving a bitmapped graphic image from one screen location to another.
The following shifts an array of 3 doublewords 1 bit to the right (view complete source code):
.data
ArraySize = 3
array DWORD ArraySize DUP(99999999h) ; 1001 1001...
.code
mov esi,0
shr array[esi + 8],1 ; high dword
rcr array[esi + 4],1 ; middle dword, include Carry
rcr array[esi],1 ; low dword, include Carry

## Slide 28: Binary Multiplication
mutiply 123 * 36

## Slide 29: Binary Multiplication
We already know that SHL performs unsigned multiplication efficiently when the multiplier is a power of 2.
You can factor any binary number into powers of 2.
  For example, to multiply EAX * 36, factor 36 into 32 + 4 and use the distributive property of multiplication to carry out the operation:
EAX * 36
= EAX * (32 + 4)
= (EAX * 32)+(EAX * 4)
mov eax,123
mov ebx,eax
shl eax,5 ; mult by 25
shl ebx,2 ; mult by 22
add eax,ebx

## Slide 30: Your turn . . .
mov ax,2 ; test value
mov dx,ax
shl dx,4 ; AX * 16
push edx ; save for later
mov dx,ax
shl dx,3 ; AX * 8
shl ax,1 ; AX * 2
add ax,dx ; AX * 10
pop edx ; recall AX * 16
add ax,dx ; AX * 26
Multiply AX by 26, using shifting and addition instructions. Hint: 26 = 16 + 8 + 2.

## Slide 31: Displaying Binary Bits
Algorithm: Shift MSB into the Carry flag; If CF = 1, append a "1" character to a string; otherwise, append a "0" character. Repeat in a loop, 32 times.
.data
buffer BYTE 32 DUP(0),0
.code
mov ecx,32
mov esi,OFFSET buffer
L1: shl eax,1
mov BYTE PTR [esi],'0'
jnc L2
mov BYTE PTR [esi],'1'
L2: inc esi
loop L1

## Slide 32: Isolating a Bit String
The MS-DOS file date field packs the year, month, and day into 16 bits:
mov ax,dx ; make a copy of DX
shr ax,5 ; shift right 5 bits
and al,00001111b ; clear bits 4-7
mov month,al ; save in month variable
Isolate the Month field:

## Slide 33: What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and Unpacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 34: Multiplication and Division Instructions
MUL Instruction
IMUL Instruction
DIV Instruction
Signed Integer Division
CBW, CWD, CDQ Instructions
IDIV Instruction
Implementing Arithmetic Expressions

## Slide 35: MUL Instruction
The MUL (unsigned multiply) instruction multiplies an 8-, 16-, or 32-bit operand by either AL, AX, or EAX.
The instruction formats are:
    MUL r/m8
    MUL r/m16
    MUL r/m32

## Slide 36: MUL Examples
100h * 2000h, using 16-bit operands:
.data
val1 WORD 2000h
val2 WORD 100h
.code
mov ax,val1
mul val2 ; DX:AX = 00200000h, CF=1
The Carry flag indicates whether or not the upper half of the product contains significant digits.
mov eax,12345h
mov ebx,1000h
mul ebx ; EDX:EAX = 0000000012345000h, CF=0
12345h * 1000h, using 32-bit operands:

## Slide 37: Your turn . . .
mov ax,1234h
mov bx,100h
mul bx
What will be the hexadecimal values of DX, AX, and the Carry flag after the following instructions execute?
DX = 0012h, AX = 3400h, CF = 1

## Slide 38: Your turn . . .
mov eax,00128765h
mov ecx,10000h
mul ecx
What will be the hexadecimal values of EDX, EAX, and the Carry flag after the following instructions execute?
EDX = 00000012h, EAX = 87650000h, CF = 1

## Slide 39: IMUL Instruction
IMUL (signed integer multiply ) multiplies an 8-, 16-, or 32-bit signed operand by either AL, AX, or EAX
Preserves the sign of the product by sign-extending it into the upper half of the destination register
Example: multiply 48 * 4, using 8-bit operands:
mov al,48
mov bl,4
imul bl ; AX = 00C0h, OF=1
OF=1 because AH is not a sign extension of AL.

## Slide 40: IMUL Examples
Multiply 4,823,424 * -423:
mov eax,4823424
mov ebx,-423
imul ebx ; EDX:EAX = FFFFFFFF86635D80h, OF=0
OF=0 because EDX is a sign extension of EAX.

## Slide 41: Your turn . . .
mov ax,8760h
mov bx,100h
imul bx
What will be the hexadecimal values of DX, AX, and the Carry flag after the following instructions execute?
DX = FF87h, AX = 6000h, OF = 1

## Slide 42: DIV Instruction
The DIV (unsigned divide) instruction performs 8-bit, 16-bit, and 32-bit division on unsigned integers
A single operand is supplied (register or memory operand), which is assumed to be the divisor
Instruction formats:
    DIV reg/mem8
    DIV reg/mem16
    DIV reg/mem32
Default Operands:

## Slide 43: DIV Examples
Divide 8003h by 100h, using 16-bit operands:
mov dx,0 ; clear dividend, high
mov ax,8003h ; dividend, low
mov cx,100h ; divisor
div cx ; AX = 0080h, DX = 3
Same division, using 32-bit operands:
mov edx,0 ; clear dividend, high
mov eax,8003h ; dividend, low
mov ecx,100h ; divisor
div ecx ; EAX = 00000080h, DX = 3

## Slide 44: Your turn . . .
mov dx,0087h
mov ax,6000h
mov bx,100h
div bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:
DX = 0000h, AX = 8760h

## Slide 45: Your turn . . .
mov dx,0087h
mov ax,6002h
mov bx,10h
div bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:
Divide Overflow

## Slide 46: Signed Integer Division (IDIV)
Signed integers must be sign-extended before division takes place
  fill high byte/word/doubleword with a copy of the low byte/word/doubleword's sign bit
For example, the high byte contains a copy of the sign bit from the low byte:

## Slide 47: CBW, CWD, CDQ Instructions
The CBW, CWD, and CDQ instructions provide important sign-extension operations:
  CBW (convert byte to word) extends AL into AH
  CWD (convert word to doubleword) extends AX into DX
  CDQ (convert doubleword to quadword) extends EAX into EDX
Example:
    .data
    dwordVal SDWORD -101 ; FFFFFF9Bh
    .code
    mov eax,dwordVal
    cdq ; EDX:EAX = FFFFFFFFFFFFFF9Bh

## Slide 48: IDIV Instruction
IDIV (signed divide) performs signed integer division
Same syntax and operands as DIV instruction
Example: 8-bit division of –48 by 5
mov al,-48
cbw ; extend AL into AH
mov bl,5
idiv bl ; AL = -9, AH = -3

## Slide 49: IDIV Examples
Example: 32-bit division of –48 by 5
mov eax,-48
cdq ; extend EAX into EDX
mov ebx,5
idiv ebx ; EAX = -9, EDX = -3
Example: 16-bit division of –48 by 5
mov ax,-48
cwd ; extend AX into DX
mov bx,5
idiv bx ; AX = -9, DX = -3

## Slide 50: Your turn . . .
mov ax,0FDFFh ; -513
cwd
mov bx,100h
idiv bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:
DX = FFFFh (-1), AX = FFFEh (-2)

## Slide 51: Unsigned Arithmetic Expressions
Some good reasons to learn how to implement integer expressions:
  Learn how do compilers do it
  Test your understanding of MUL, IMUL, DIV, IDIV
  Check for overflow (Carry and Overflow flags)
Example: var4 = (var1 + var2) * var3
; Assume unsigned operands
mov eax,var1
add eax,var2 ; EAX = var1 + var2
mul var3 ; EAX = EAX * var3
jc TooBig ; check for carry
mov var4,eax ; save product

## Slide 52: Signed Arithmetic Expressions (1 of 2)
Example: eax = (-var1 * var2) + var3
mov eax,var1
neg eax
imul var2
jo TooBig ; check for overflow
add eax,var3
jo TooBig ; check for overflow
Example: var4 = (var1 * 5) / (var2 – 3)
mov eax,var1 ; left side
mov ebx,5
imul ebx ; EDX:EAX = product
mov ebx,var2 ; right side
sub ebx,3
idiv ebx ; EAX = quotient
mov var4,eax

## Slide 53: Signed Arithmetic Expressions (2 of 2)
Example: var4 = (var1 * -5) / (-var2 % var3);
mov eax,var2 ; begin right side
neg eax
cdq ; sign-extend dividend
idiv var3 ; EDX = remainder
mov ebx,edx ; EBX = right side
mov eax,-5 ; begin left side
imul var1 ; EDX:EAX = left side
idiv ebx ; final division
mov var4,eax ; quotient
Sometimes it's easiest to calculate the right-hand term of an expression first.

## Slide 54: Your turn . . .
mov eax,20
imul ebx
idiv ecx
Implement the following expression using signed 32-bit integers:
eax = (ebx * 20) / ecx

## Slide 55: Your turn . . .
push edx
push eax ; EAX needed later
mov eax,ecx
imul edx ; left side: EDX:EAX
pop ebx ; saved value of EAX
idiv ebx ; EAX = quotient
pop edx ; restore EDX, ECX
Implement the following expression using signed 32-bit integers. Save and restore ECX and EDX:
eax = (ecx * edx) / eax

## Slide 56: Your turn . . .
mov eax,var1
mov edx,var2
neg edx
imul edx ; left side: EDX:EAX
mov ecx,var3
sub ecx,ebx
idiv ecx ; EAX = quotient
mov var3,eax
Implement the following expression using signed 32-bit integers. Do not modify any variables other than var3:
var3 = (var1 * -var2) / (var3 – ebx)

## Slide 57: What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and UnPacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 58: Extended Addition and Subtraction
ADC Instruction
Extended Precision Addition
SBB Instruction
Extended Precision Subtraction

## Slide 59: Extended Precision Addition
Adding two operands that are longer than the computer's word size (32 bits).
  Virtually no limit to the size of the operands
The arithmetic must be performed in steps
  The Carry value from each step is passed on to the next step.

## Slide 60: ADC Instruction
ADC (add with carry) instruction adds both a source operand and the contents of the Carry flag to a destination operand.
Operands are binary values
  Same syntax as ADD, SUB, etc.
Example
  Add two 32-bit integers (FFFFFFFFh + FFFFFFFFh), producing a 64-bit sum in EDX:EAX:
    mov edx,0
    mov eax,0FFFFFFFFh
    add eax,0FFFFFFFFh
    adc edx,0 ;EDX:EAX = 00000001FFFFFFFEh

## Slide 61: Extended Addition Example
Task: Add 1 to EDX:EAX
  Starting value of EDX:EAX: 00000000FFFFFFFFh
  Add the lower 32 bits first, setting the Carry flag.
  Add the upper 32 bits, and include the Carry flag.
mov edx,0 ; set upper half
mov eax,0FFFFFFFFh ; set lower half
add eax,1 ; add lower half
adc edx,0 ; add upper half
    EDX:EAX = 00000001 00000000

## Slide 62: SBB Instruction
The SBB (subtract with borrow) instruction subtracts both a source operand and the value of the Carry flag from a destination operand.
Operand syntax:
  Same as for the ADC instruction

## Slide 63: Extended Subtraction Example
Task: Subtract 1 from EDX:EAX
  Starting value of EDX:EAX: 0000000100000000h
  Subtract the lower 32 bits first, setting the Carry flag.
  Subtract the upper 32 bits, and include the Carry flag.
mov edx,1 ; set upper half
mov eax,0 ; set lower half
sub eax,1 ; subtract lower half
sbb edx,0 ; subtract upper half
EDX:EAX = 00000000 FFFFFFFF

## Slide 64: Summary
Shift and rotate instructions are some of the best tools of assembly language
  finer control than in high-level languages
  SHL, SHR, SAR, ROL, ROR, RCL, RCR
MUL and DIV – integer operations
  close relatives of SHL and SHR
  CBW, CDQ, CWD: preparation for division
Extended precision arithmetic: ADC, SBB
ASCII decimal operations (AAA, AAS, AAM, AAD)
Packed decimal operations (DAA, DAS)

## Slide 65: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only